## Slide 1: TX FIR Equalizer – CML mode
12 Gbps
(Final Report)
Muhammad Aldacher

## Slide 2: Outline
Background
Implementation
Schematics
Design Steps
Simulation Results
  Pulse Response
  Eye Diagram
  Transient Waveforms

## Slide 3: Background
"TX FIR equalization" is the technique in which a transmitter applies a Finite Impulse Response (FIR) filter to pre-distort the signal before sending it.
This is to compensate for the distortions introduced by the transmission channel, thus improving signal quality at the receiver by mitigating intersymbol interference (ISI).

## Slide 4: Background
Input Pulse w/ 3-tap TX Eq
Output Pulse Response
Time Domain

## Slide 5: Background
Freq Domain
Channel Response w/ TX FIR Eq

## Slide 6: Implementation
For CML driver:

## Slide 7: Implementation
For CML driver:

## Slide 8: Schematics
FIR logic
CML Driver
Channel & Load

## Slide 9: Schematics
A) FIR Logic:
Pre-Cursor 1
Main-Cursor
Post-Cursor 1
Post-Cursor 2
12 Gb/s PRBS Inputs
12 GHz Clock
Flipflops used to align the input data to the FF edges
Flipflops used as delay cells
XOR gates used to apply the sign to the cursor taps

## Slide 10: Schematics
B) CML Driver:
m=12 L=4*LMIN
m=200 L=4*LMIN
m=58 L=4*LMIN
m=28 L=4*LMIN
IPRE1=0.6mA
IMAIN=10mA
IPOST1=2.9mA
IPOST2=1.4mA
m=200 L=4*LMIN
Pre1
Main
Post1
Post2
m=100 L=LMIN
m=100 L=LMIN
m=100 L=LMIN
m=100 L=LMIN

## Slide 11: Schematics
C) Channel & Load:
1-inch FR4 section

## Slide 12: Design Steps
Design the Tx-Driver at a low data-rate & without equalization as shown in this project (Tx-Driver Design)
Plot the pulse response of this Tx-Driver at the desired data-rate.
Calculate the pre & post cursors from the pulse response.
Modify the Tx-Driver design by adding weighted taps based on the cursors’ values.
Plot the eye diagram to see how much the eye opening improved.

## Slide 13: Design Parameters
Parameter | Value
Data Rate | 12 Gb/s
VDD | 1 V
Tx-Driver | Current Mode (CML)
VSWING (PK2PK) | 0.5 V
IBIAS | 10mA
Channel | 12-inch FR4

## Slide 14: Simulation Results
A) Pulse Response:
(Without Equalization)
Pre-Cursor1 = 18mV
Main-Cursor = 303mV
Post-Cursor1 = 88mV
Post-Cursor2 = 42mV
 | Pre- Cursor1 | Main- Cursor | Post- Cursor1 | Post- Cursor2
Adjusted VSWING(PK2PK) | (18 / 303) * 500 mV = 29.7 mV | (303 / 303) * 500 mV = 500 mV | (88 / 303) * 500 mV = 145.2 mV | (42 / 303) * 500 mV = 69.3 mV
Equivalent IBIAS | 29.7 mV / 50 Ohms = 0.6 mA | 500 mV / 50 Ohms = 10 mA | 145.2 mV / 50 Ohms = 2.9 mA | 69.3 mV / 50 Ohms = 1.4 mA
# of fingers | (m = 12) | (m = 200) | (m = 58) | (m = 28)

## Slide 15: Simulation Results
A) Pulse Response:
(With Equalization)
No Equalization
Pre-Cursor1 Eq only
Post-Cursor1 Eq only
Post-Cursor2 Eq only
4-tap Eq (1pre, main, 2post)

## Slide 16: Simulation Results
B) Eye Diagram:
(Without Equalization)
103.1 mV
38.69 ps

## Slide 17: Simulation Results
B) Eye Diagram:
(With Equalization)
223.3 mV
73.38 ps

## Slide 18: Simulation Results
B) Eye Diagram:
 | No Equalization | With Equalization (4-tap)
Eye Height (Max) | 103.1 mV | 223.3 mV
Eye Width (Max) | 38.69 ps | 73.38 ps
Swing (PK2PK) | 500 mV (–250mV ~ +250mV) | 328 mV (–164mV ~ +164mV)

## Slide 19: Simulation Results
C) Transient Waveforms:
(Without Equalization)

## Slide 20: Simulation Results
C) Transient Waveforms:
(With Equalization)

## Slide 21: Simulation Results
C) Transient Waveforms:
(With Equalization)

## Slide 22: Conclusion
This project shows the design procedure of a TX FIR Equalizer for a 12 Gb/s input & a channel of 12-inch FR4.
It also shows how the equalization improves the eye opening of the output, while paying the price of lower swing amplitude & increased latency.