## Slide 1: TX FIR Equalizer
12 Gbps
(Eye Diagram)
Muhammad Aldacher

## Slide 2: Design Parameters
Parameter | Value
Data Rate | 12 Gb/s
VDD | 1 V
Tx-Driver | Current Mode (CML)
VSWING (PK2PK) | 0.5 V
IBIAS | 10mA
Channel | 12-inch FR4

## Slide 3: Channel = 12 x 1-inch FR4 section
1-inch FR4 section

## Slide 4: 1) Eye Diagram (without Equalization)

## Slide 5: TB Schematics
m=200 L=4*LMIN
m=200 L=4*LMIN
m=100 L=LMIN
m=100 L=LMIN
IMAIN=10mA
LIB: analogLib
CELL: vprbs
Zero value: 0 V / 1 V
One value: 1 V / 0 V
Bit period: 83.33ps (1/12G)
Rise/Fall times: 2.5 ps
Edge type: linear
Trigger: Internal
LFSR Mode: PN32

## Slide 6: Analysis Setup
Eye Diagram

## Slide 7: Eye Diagram
Measurements  Eye Diagram
103.1 mV
38.69 ps

## Slide 8: 2) Eye Diagram (with Equalization)

## Slide 9: TB Schematics
m=12 L=4*LMIN
m=200 L=4*LMIN
m=58 L=4*LMIN
m=28 L=4*LMIN
IPRE1=0.6mA
IMAIN=10mA
IPOST1=2.9mA
IPOST2=1.4mA
m=200 L=4*LMIN
Pre1
Main
Post1
Post2

## Slide 10: TB Schematics
LIB: analogLib
CELL: vprbs
Zero value: 0 V / 1 V
One value: 1 V / 0 V
Bit period: 83.33ps (1/12G)
Rise/Fall times: 2.5 ps
Edge type: linear
Trigger: Internal
LFSR Mode: PN32
LIB: ahdlLib
CELL: d_ff
Vlogic_high/low: 1/0
Vtrans_clk/Vtrans: 0.5
tdel: 1f
Rise/Fall times: 2.5 ps
LIB: ahdlLib
CELL: xor_gate
Vlogic_high/low: 1/0
Vtrans: 0.5
tdel: 1f
Rise/Fall times: 2.5 ps
LIB: analogLib
CELL: vpulse
Voltage1: 1 V
Voltage2: 0 V
Period: 83.33ps (1/12G)
Rise/Fall times: 1 ps
Pulse width: 41.67ps (0.5/12G)
m=12 L=4*LMIN
m=200 L=4*LMIN
m=58 L=4*LMIN
m=28 L=4*LMIN
m=200 L=4*LMIN
(Datarate = = 12Gb/s)
(Data is sampled every = every rising edge)
Pre1
Main
Post1
Post2
IPRE1=0.6mA
IMAIN=10mA
IPOST1=2.9mA
IPOST2=1.4mA

## Slide 11: Analysis Setup
Eye Diagram
* Delay time of 10ns is added to remove any settling time issues at the beginning of the simulation.
* The Sign bit of the XOR gates is set to 1, to subtract the cursor values from the main waveform.

## Slide 12: Eye Diagram
Measurements  Eye Diagram
223.3 mV
73.38 ps

## Slide 13: Eye Diagram (Comparison)
With Equalization, the swing pk2pk amplitude is reduced but the Eye opening is improved.

## Slide 14: Eye Diagram (Comparison)
 | No Equalization | With Equalization (4-tap)
Eye Height (Max) | 103.1 mV | 223.3 mV
Eye Width (Max) | 38.69 ps | 73.38 ps
Swing (PK2PK) | 500 mV (–250mV ~ +250mV) | 328 mV (–164mV ~ +164mV)